## Slide 1: Hermes2d
C++ library for rapid development of adaptive
hp-FEM / hp-DG solvers
Lukas Korous

## Slide 2: Hermes2d Overview
What it is?
C++ multi-platform (Win, Linux, MacOS) library for rapid prototyping of FEM & DG solvers
“When you want to solve a non-trivial PDE in 2d with the least possible effort. And you know some C/C++.”
“When you want to test drive something small (a preconditioner, error estimate, FE space), and you don’t want to write all the rest for it. And you know some OOP in C++.”
How can I try it out?
https://github.com/hpfem/hermes
On Linux
  Download, get dependencies via package managers, configure, build
On Windows
  Download, get dependencies from https://github.com/l-korous/hermes-windows, configure, build
What technologies are used in Hermes2d?
(Modern) C++, well documented, and exception-safe
OpenMP for parallelization of the most CPU-intensive tasks
Real-time OpenGL visualization
External linear solvers (UMFPACK, PARALUTION, MUMPS, PETSc)
Usual exchange formats (XML, BSON, VTK, ExodusII, MatrixMarket, Matlab)
Hermes2D – Lukas Korous

## Slide 3: Hermes2d Overview > Features
What can it do?
Stationary / Time-dependent / Harmonic equations
Number of manual, and automatic mesh refinement (AMR) options
  Granular AMR setup based on customizable error estimate calculations
Nonlinear equation handling using Newton’s and Picard’s method
  Fully automatic & configurable Newton’s method with damping coefficient control, jacobian reuse control, arbitrary stopping criteria control
Time-adaptivity, Space-time adaptivity using embedded Runge-Kutta methods
  Time-error space distribution, arbitrary calculations of any error estimate pluggable into AMR, and time-step controllers
Weak & Strong coupled problems
  No matter what the coupling is, when you can write the weak formulation of your problem on paper, you can do that in Hermes2d as well.
What it cannot do (does not do)
Problem specific optimizations, caching, shortcuts, etc.
  But #1: In some cases, the Hermes2D API provides methods that can be used for some optimizations.
  But #2: Due to the use of OOP, users of the library are welcome to sub-class Hermes2d core classes and implement the missing functionality.
Hermes2D – Lukas Korous

## Slide 4: Examples > Magnetostatics
In this example, we solve the equation
Where
J is the current density,
is (nonlinear) permeability,
u is the (sought) magnetic vector potential (its z-component),
is the space domain (picture on next slide).
The features illustrated on this example are
Newton’s method for nonlinear problems,
nonlinear term specification using a table of values, and cubic spline interpolation.
Hermes2D – Lukas Korous

## Slide 5: Examples > Magnetostatics
Hermes2D – Lukas Korous
Domain with
triangular mesh
Solution –
vector potential u

## Slide 6: Examples > Magnetostatics
Refining the mesh according to a criterion
  mesh->refine_by_criterion(&refinement_criterion);
  - header: int refinement_criterion(Element* e), returning whether or not to refine a particular Element.
  Used to refine the mesh in the TODO – DOPLNIT
CubicSpline class used for nonlinearity description
  // Define nonlinear magnetic permeability via a cubic spline.
  std::vector<double> mu_inv_pts({ 0.0, 0.5, 0.9, ... });
  std::vector<double> mu_inv_val({ 1. / 1500.0, 1. / 1480.0, 1. / 1440.0, ... });
  CubicSpline mu_inv_iron(mu_inv_pts, mu_inv_val, ...);
Newton’s method for a strong nonlinearity
  // Automatic damping ratio – if a step is unsuccessful, damping factor will be multiplied by this, if successful, it will be divided by this.
  newton.set_auto_damping_ratio(1.5);
  // Initial damping factor – we can start with a small one, automation will increase it if possible.
  newton.set_initial_auto_damping_coeff(.1);
  // The redidual norm after a step must be at most this factor times the norm from the previous step to pronounce the step ‘successful’.
  // Now for very strong nonlinearities, we may even need this > 1.
  newton.set_sufficient_improvement_factor(1.25);
  // This is a strong nonlinearity, where we can’t afford to reuse Jacobian matrix from a step in subsequent steps.
  newton.set_max_steps_with_reused_jacobian(0);
  // Maximum number of iterations. Hermes will throw an exception if this number is exceeded and the tolerance is not met.
  newton.set_max_allowed_iterations(100);
  // The tolerance – simple in this case, but can be a combination of relative / absolute thresholds of residual norm, solution norm, solution difference norm, ...
  newton.set_tolerance(1e-8, Hermes::Solvers::ResidualNormAbsolute);
Hermes2D – Lukas Korous

## Slide 7: Examples > Advection
In this example, we solve the equation
Where
u is the sought solution,
is the space domain - square (0, 1) x (0, 1),
g is defined as follows:
  ,
  .
The features illustrated on this example are
Discontinuous Galerkin (DG) implementation of integrating over internal edges,
postprocessing of results – in this case using a limiter preventing spurious oscillations that occur in DG method.
Hermes2D – Lukas Korous

## Slide 8: Examples > Advection
Hermes2D – Lukas Korous
Domain with
quadrilateral mesh
Solution

## Slide 9: Examples > Advection
Integration over internal edges
Regular forms (simplified)
  matrix_form(int n, double *wt, Func<double> *u, Func<double> *v)
  n ... Number of integration points
  wt ... Integration weights
  u ... Basis function values(, derivatives) in the integration points
  v ... Test function values(, derivatives) in the integration points
DG forms (simplified)
  matrix_form(int n, double *wt, DiscontinuousFunc<double> *u, DiscontinuousFunc<double> *v)
  n, wt ... As above
  u, v ... DiscontinuousFunc<double> = { Func<double> u->central, Func<double>* u->neighbor } ... Only one is filled for each matrix_form call.
Postprocessing
e.g. Vertex-based limiter (Kuzmin, D.: A vertex-based hierarchical slope limiter for -adaptive discontinuous Galerkin methods, JCAM, 233(12):3077-3085)
  // sln_vector ... Algebraic system solution
  // space ... FE space of the solution
  // Instantiate the limiter
  PostProcessing::VertexBasedLimiter limiter(space, sln_vector);
  // Get a limited solution, already as a Hermes2D Solution object
  Hermes::Hermes2D::Solution<double> limited_sln = limiter.get_solution();
Hermes2D – Lukas Korous

## Slide 10: Examples > Advection > Automatic adaptivity (AMR)
We solve the same problem – equation & boundary conditions:
But this time, we start from a very coarse mesh:
And we employ AMR (h-adaptivity) to get results on the next slide.
Hermes2D – Lukas Korous

## Slide 11: Examples > Advection > Automatic adaptivity (AMR)
Hermes2D – Lukas Korous
AMR step 1, Element count: 32
AMR step 2, Element count: 116
AMR step 3, Element count: 272
AMR step 4, Element count: 504
AMR step 5, Element count: 848

## Slide 12: Examples > Advection > Automatic adaptivity (AMR)
int adaptivity_step = 1; bool done = false;
do
{
// Construct globally refined reference mesh and setup reference space.
Mesh::ReferenceMeshCreator ref_mesh_creator(mesh);
MeshSharedPtr ref_mesh = ref_mesh_creator.create_ref_mesh();
Space<double>::ReferenceSpaceCreator refspace_creator(space, ref_mesh, USE_TAYLOR_SHAPESET ? 0 : 1);
SpaceSharedPtr<double> refspace = refspace_creator.create_ref_space();
// Solve the problem on the reference space.
linear_solver.set_space(refspace);
linear_solver.solve();
// Get the Hermes2D Solution object from the solution vector.
Solution<double>::vector_to_solution(linear_solver.get_sln_vector(), refspace, refsln);
// Project the reference solution to the coarse space in L2 norm for error calculation.
OGProjection<double>::project_global(space, refsln, sln, HERMES_L2_NORM);
// Calculate element errors and total error estimate.
errorCalculator.calculate_errors(sln, refsln);
double total_error_estimate = errorCalculator.get_total_error_squared() * 100;
// If error is too large, adapt the (coarse) space.
if (error_estimate > ERR_STOP)
adaptivity.adapt(&selector);
else
done = true;
// Increase the step counter.
adaptivity_step++;
} while (done == false);
Hermes2D – Lukas Korous

## Slide 13: Examples > Navier-Stokes
In this example, we solve the equations
Where
is the output boundary,
u, p is the sought solution,
is the space domain – see next slide,
g is defined as follows:
  everywhere except inlet,
  everywhere,
  is a parabolic profile on the inlet.
The features illustrated on this example are
OpenGL visualization of vector fields,
Simple time-stepping using implicit Euler scheme.
Hermes2D – Lukas Korous

## Slide 14: Examples > Navier-Stokes > OpenGL visualization of vector fields
Solution
Velocity (vector field) top
Pressure bottom
t = 30s
Hermes2D – Lukas Korous

## Slide 15: Examples > Navier-Stokes > OpenGL visualization of vector fields
Solution
Velocity (vector field) top
Pressure bottom
t = 40s
Hermes2D – Lukas Korous

## Slide 16: Examples > Navier-Stokes > OpenGL visualization of vector fields
Solution
Velocity (vector field) top
Pressure bottom
t = 55s
Hermes2D – Lukas Korous

## Slide 17: Examples > Navier-Stokes
Simple time-stepping using implicit Euler scheme
  for (int time_step = 1; time_step <= T_FINAL / TAU; time_step++, current_time += TAU)
  {
  // Update time-dependent essential BCs.
  newton.set_time(current_time);
  // Solve Newton.
  // Weak formulation implements the implicit Euler scheme, and uses previous time step solutions.
  newton.solve(coeff_vec);
  // Get the solutions, insert as Hermes2D Solution object into the previous time step solutions.
  Hermes::Hermes2D::Solution<double>::vector_to_solutions(newton.get_sln_vector(), spaces, sln_prev_time);
  // Visualization.
  vview.set_title("Velocity, time %g", current_time);
  vview.show(xvel_prev_time, yvel_prev_time);
  pview.set_title("Pressure, time %g", current_time);
  pview.show(p_prev_time);
  }
Hermes2D – Lukas Korous

## Slide 18: Example > Complex
This problem describes the distribution of the vector potential in a domain comprising a wire carrying electrical current, air, and an iron which is not under voltage. We solve the equation
Where
is the space domain - rectangle (0, 0.004) x (0, 0.003),
is the top and right and left edge of ,
is the bottom edge of ,
A is the sought solution, is the given angular velocity, given permittivity TODO – je to tak?
The features illustrated on this example are
hp-adaptive FEM,
Handling of complex equations in Hermes2D,
Spatial error inspection.
Hermes2D – Lukas Korous

## Slide 19: Example > Complex > hp-FEM step #1
Hermes2D – Lukas Korous
Solution
Reference space
Coarse mesh
Fine mesh
Spatial error inspection
Element-wise error for the coarse mesh

## Slide 20: Example > Complex > hp-FEM step #5
Hermes2D – Lukas Korous
Solution
Reference space
Coarse mesh
Fine mesh
Spatial error inspection
Element-wise error for the coarse mesh

## Slide 21: Example > Complex > hp-FEM step #15
Hermes2D – Lukas Korous
Solution
Reference space
Coarse mesh
Fine mesh
Spatial error inspection
Element-wise error for the coarse mesh

## Slide 22: Example > Complex > hp-FEM step #29
Hermes2D – Lukas Korous
Solution
Reference space
Coarse mesh
Fine mesh
Spatial error inspection
Element-wise error for the coarse mesh

## Slide 23: Example > Complex
Handling of complex equations in Hermes2D
Very easy, all relevant Hermes2d classes have the number (real | complex) as their template argument:
  For real numbers we use double: H1Space<std::complex<double> >(mesh, boundary_conditions)
  For complex numbers we use std::complex<double>: H1Space<std::complex<double> >(mesh, boundary_conditions)
hp-adaptive FEM
Basic settings to control the AMR process
  // Error calculation & adaptivity. We specify the norm here, and the type of error
  DefaultErrorCalculator<::complex, HERMES_H1_NORM> errorCalculator(RelativeErrorToGlobalNorm);
  // Stopping criterion for an adaptivity step. Influences the number of elements refined at each step.
  AdaptStoppingCriterionSingleElement<::complex> stoppingCriterion(0.9);
  // Adaptivity processor class. Gets the error calculator and stopping criterion
  Adapt<::complex> adaptivity(&errorCalculator, &stoppingCriterion);
  // Stopping criterion for adaptivity.
  const double TOTAL_ERROR_ESTIMATE_STOP = 1e-3;
Hermes2D – Lukas Korous

## Slide 24: Examples > Wave Equation
In this example, we solve the equations
Where
u is the sought solution,
is the space domain – see next slide,
c is the wave speed.
We transform (1) into
The features illustrated on this example are
Using an arbitrary Runge-Kutta method for time discretization,
Time-adaptivity using embedded Runge-Kutta methods.
Hermes2D – Lukas Korous

## Slide 25: Example > Wave Equation
Hermes2D – Lukas Korous
u (left), v(right), t = 1e-2s

## Slide 26: Example > Wave Equation
Hermes2D – Lukas Korous
u (left), v(right), t = 5.1e-1s

## Slide 27: Example > Wave Equation
Hermes2D – Lukas Korous
u (left), v(right), t = 1.01s

## Slide 28: Example > Wave Equation
Hermes2D – Lukas Korous
u (left), v(right), t = 1.51s

## Slide 29: Example > Wave Equation
Hermes2D – Lukas Korous
u (left), v(right), t = 2.01s

## Slide 30: Example > Wave Equation
Time-adaptivity using embedded Runge-Kutta methods
  runge_kutta.rk_time_step_newton(previous_solution, new_solution, time_error_function);
  ...
  Hermes::Hermes2D::Views::ScalarView time_error_view;
  time_error_view.show(time_error_function);
  ...
  DefaultNormCalculator<double, HERMES_H1_NORM> normCalculator;
  normCalculator.calculate_norms(time_error_function);
  double relative_time_error_estimate = normCalculator.get_total_norm_squared() * 100.;
  Image – temporal error in u (top), v (bottom), t = 0.3s
Hermes2D – Lukas Korous

## Slide 31: Example > Wave Equation
Time-adaptivity using embedded Runge-Kutta methods
  runge_kutta.rk_time_step_newton(previous_solution, new_solution, time_error_function);
  ...
  Hermes::Hermes2D::Views::ScalarView time_error_view;
  time_error_view.show(time_error_function);
  ...
  DefaultNormCalculator<double, HERMES_H1_NORM> normCalculator;
  normCalculator.calculate_norms(time_error_function);
  double relative_time_error_estimate = normCalculator.get_total_norm_squared() * 100.;
  Image – temporal error in u (top), v (bottom), t = 0.8s
Hermes2D – Lukas Korous

## Slide 32: Example > Benchmark Interior Layer
We solve the equation
Where
is the space domain - square (0, 1) x (0, 1),
is the (known) exact solution,
is the Laplacian of the exact solution,
u is the sought solution
The features illustrated on this example are
Calculating exact error,
Anisotropic refinements usage in AMR.
Hermes2D – Lukas Korous

## Slide 33: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #1

## Slide 34: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #2

## Slide 35: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #3

## Slide 36: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #6

## Slide 37: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #11

## Slide 38: Example > Benchmark Interior Layer
Hermes2D – Lukas Korous
solution (left), FE space (right), adaptivity step #19

## Slide 39: Example > Benchmark Interior Layer
Calculating exact error – through sub-classing existing Hermes2D class ExactSolutionScalar<double>:
  class CustomExactSolution : public ExactSolutionScalar<double>{
  public:
  // Implement the actual function expression.
  virtual double value(double x, double y) const;
  // Implement the derivatives expression.
  virtual void derivatives (double x, double y, double& dx, double& dy) const;
  // Overwrite the expression calculating polynomial order (for integration order deduction).
  virtual Ord value(Ord x, Ord y) const;
  };
and then employing standard ErrorCalculator<double> class for error calculation
Anisotropic refinements usage in AMR
  // Predefined list of element refinement candidates.
  // H2D_HP_ANISO stands for h-, and p-candidates, anisotropic in shape, and polynomial orders.
  const CandList CAND_LIST = H2D_HP_ANISO;
  // Class which for each element selected for refinement, selects the best refinement candidate.
  H1ProjBasedSelector<double> selector(CAND_LIST);
  ...
  // As before, adapt the FE space – using the selector provided
  adaptivity.adapt(&selector);
Hermes2D – Lukas Korous

## Slide 40: Example > Heat and Moisture
We solve the system of equations
Where
is the sought solution,
are thermal capacity and thermal conductivity properties,
(complicated) boundary conditions (Axisymmetric, Dirichlet, Newton)
The features illustrated on this example are
Multimesh,
Dynamical meshes.
Hermes2D – Lukas Korous

## Slide 41: Example > Heat and Moisture
Hermes2D – Lukas Korous
Meshes for T, w (left); Solutions for T, w (right).

## Slide 42: Example > Heat and Moisture
Multimesh & Dynamical meshes
  The key functionality here is de-refining the FE space, either periodically or when some indicator indicates us to.
  if (should_unrefine_in_this_step)
  {
  // Unrefine one layer of refinements on the mesh for T.
  T_mesh->unrefine_all_elements();
  // Also coarsen the polynomial order.
  T_space->adjust_element_order(-1);
  // Do the above also for the mesh for w.
  w_mesh->unrefine_all_elements();
  w_space->adjust_element_order(-1);
  // Assign DOFs after the change.
  T_space->assign_dofs();
  w_space->assign_dofs();
  }
Note:
  In the above, it is clearly seen that there are two Space, and two Mesh structures – different for each component.
  This is enough input from the user to achieve multi-mesh behavior. Hermes2D takes care of the rest.
Hermes2D – Lukas Korous

## Slide 43: Example > GAMM channel
We solve the Euler equations of compressible flow
Where
w is the sought solution,
are constants
(complicated) Boundary conditions are reflective, ‘do nothing’, and inlet
The feature illustrated on this example are:
- Postprocessing filters (calculating Mach number, pressure)
Hermes2D – Lukas Korous